## Slide 1: Digital Design Primer
FPGA/Verilog from Scratch
DAY 1

## Slide 2: Outline
Digital Systems
Binary Numbers
Number-base Conversions
Signed Numbers
Binary Logic

## Slide 3: Digital systems
Analog Systems
  The physical quantities or signals may vary continuously over a specified range.
Digital Systems
  The physical quantities or signals can assume only discrete values.
Analog signal
t
X(t)
Digital signal
X(t)
t

## Slide 4: Binary Numbers
For digital systems, the variable takes on discrete values.
  Two level, or binary values are the most prevalent values.
  Any number can be represented in binary format
  ex: 67 = (0100 0011)2
  The power of 2
n | 2n
0 | 20=1
1 | 21=2
2 | 22=4
3 | 23=8
4 | 24=16
5 | 25=32
6 | 26=64
7 | 27=128
n | 2n
8 | 28=256
9 | 29=512
10 | 210=1024
11 | 211=2048
12 | 212=4096
20 | 220=1M
30 | 230=1G
40 | 240=1T

## Slide 5: Number-base Conversions
Decimal to Binary conversion
  Divide the number by the ‘Base’ (=2)
  Take the remainder (either 0 or 1) as a coefficient
  Take the quotient and repeat the division
  Example: (13)10
Quotient
Remainder
Coefficient
Answer: (13)10 = (a3 a2 a1 a0)2 = (1101)2
MSB LSB
13
/ 2 = 6
1 a0 = 1
6
/ 2 = 3
0 a1 = 0
3
/ 2 = 1
1 a2 = 1
1
/ 2 = 0
1 a3 = 1

## Slide 6: Number-base Conversions
Binary to Decimal Conversion
  Start from the right most digit
  Next, multiply this with the power of 2, and add the result.
  Continue this process until there are no more digits left.
= 0 + 2 + 0 + 8 = 10

## Slide 7: Number-base Conversions
Decimal | Binary | Hex
00 | 0000 | 0
01 | 0001 | 1
02 | 0010 | 2
03 | 0011 | 3
04 | 0100 | 4
05 | 0101 | 5
06 | 0110 | 6
07 | 0111 | 7
08 | 1000 | 8
09 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F

## Slide 8: Signed numbers
1’s Complement
  All ‘0’s become ‘1’s
  All ‘1’s become ‘0’s
  Example (10110000)2
   (01001111)2
  2’s Complement
    Take 1’s complement then add 1
    Toggle all bits to the left of the first ‘1’ from the right
  Number: (10110000)2
  1’s Comp.: (01001111)2
  ( 1)2
  2’s Comp.: (01010000)2

## Slide 9: Signed numbers
Given the two binary numbers X = 1010100 and Y = 1000011, perform the subtraction (a) X – Y (b) Y - X , by using 2's complement.
There is no carry.
Therefore, the answer is
Y – X =  (2's complement of 1101111) =  0010001.

## Slide 10: Binary logic
Binary logic consists of binary variables and a set of logical operations.
The variables are designated by letters of the alphabet, such as A, B, C, x, y, z, etc, with each variable having two and only two distinct possible values: 1 and 0
Three basic logical operations: AND, OR, and NOT.

## Slide 11: Binary logic
Truth Tables, Boolean Expressions, and Logic Gates
x | y | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | z
0 | 1
1 | 0
AND
OR
NOT
z = x • y = x y
z = x + y
z = x = x’

## Slide 12: Binary logic
Input-Output signals for gates

## Slide 13: Outline
Boolean Algebra
Boolean Functions
All Logic Gates
K-Map
Implementation with Logic Gates
Example : Parity Checking
Notes: I will talk about xxx and yy

## Slide 14: Boolean (binary) algebra
What is an algebra?
  Mathematical system consisting of
    Set of elements (example: N= {1,2,3,4,…})
    Set of operators (+, -,×,÷)
    Axioms or postulates (associativity, distributivity, closure, identityelements, etc.)
Why is it important?
  Defines rules of “calculations”
Deals with binary variables and binary logic functions.
Has two discrete values
  0, False, On
  1, True, Off
Three basic logical operations
  AND (.); OR (+); NOT (‘)
Notes: it was mentioned in the previous lessondigital systems are discrete systems.
we have 3 main operations.

## Slide 15: Boolean algebra – keywords
Literal: is a variable or its complement. ex: X, ~X, Y
Boolean Function: is a Boolean (binary) variable, which gets evaluated from logic computations involving Boolean variables and logic operators like ‘.’ AND ,’+’ OR, ‘’~’ NOT
Term: is a collection of Boolean variables formed by AND-ing or OR-ing, ex: ABC or (a+b)
Product Term: formed by AND-ing two or more Boolean variables. ex: ABC
Sum Term: formed by OR-ing two or more Boolean variables. ex: (a+b)
Sum of products: is the sum of product terms.
Canonical Form: It’s a function formed by min terms or max terms.
Min Term: It is a special product of literals, in which each input variable appears exactly once.
Max Term: It is a sum of literals , in which each input variable appears exactly once.
Truth Table: is a table that depicts the Boolean variable that has a value, 0 or 1.
Notes: the words here are your dictionary. It consists of main words in logic design courses.

## Slide 16: Boolean algebra – basic definitions
Associative Law: (x * y) * z = x * (y * z)
Commutative Law: x * y = y * x
Identity Element: e * x = x * e = x , x + 0 = 0 + x = 0 ,
  Identity elements for (+) = 0 , (.) = 1
Complement (inverse): x * y = e , x + (-x) = 0
Distributive Law: x * (y . z) = (x * y) . (x * z)
* represents the binary operators like ‘.’ , ‘+’

## Slide 17: Boolean FUNCtions
Example function is = xyz’
The is equal to 1if x=1 and y=1 and z’=1 : otherwise = 0
x | y | z | 
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
x | y | z | 
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Notes: It was the intro so far. now we can work on an example.
there are 3 literals in this example.
how many logic operators are there? Just two. Actually ıts product term (andig).
First we have to start by create the truth table.
The truth table consists of cases where the given equation is 1 and 0.
Let's consider the design part. With which logical gates can we provide this equation?

## Slide 18: Boolean functions
Simplify the Boolean function = x + x’y to a minimum number of literals.
  = x + x’y
    = x + (x’y)
    = (x + x’) . (x + y)
    = 1 . (x + y)
    = x + y

## Slide 19: Boolean functions
Example function is = x + y’z
SOP (Sum of products) form :
  = m1 + m5 + m6
  =
x | y | z |  | Corresponding minterm | designation
0 | 0 | 0 | 0 | x’y’z | 
0 | 0 | 1 | 1 | x’y’z | 
0 | 1 | 0 | 0 | x’yz’ | 
0 | 1 | 1 | 0 | x’yz | 
1 | 0 | 0 | 1 | xy’z’ | 
1 | 0 | 1 | 1 | xy’z | 
1 | 1 | 0 | 1 | xyz’ | 
1 | 1 | 1 | 1 | xyz | 
x | y | z |  | Corresponding minterm | designation
0 | 0 | 0 | 0 | x’y’z | 
0 | 0 | 1 | 1 | x’y’z | 
0 | 1 | 0 | 0 | x’yz’ | 
0 | 1 | 1 | 0 | x’yz | 
1 | 0 | 0 | 1 | xy’z’ | 
1 | 0 | 1 | 1 | xy’z | 
1 | 1 | 0 | 1 | xyz’ | 
1 | 1 | 1 | 1 | xyz | 

## Slide 20: SUMMary of Logic gates

## Slide 21: SUMMary of Logic gates

## Slide 22: Karnaugh Map ( K-map)
The k-map use for a logic minimization.
Two-variable Map
Representation of functions in the map

## Slide 23: Karnaugh Map ( K-map)
Three-variable Map

## Slide 24: Karnaugh Map ( K-map)
Example: simplify the Boolean function F(x, y, z) = S(2, 3, 4, 5)
F(x, y, z) = S(2, 3, 4, 5)
= x'y + xy’
= xy

## Slide 25: Parity checking
The problem is to show how many ones (1s) a given number contains by looking at its bits. The given number is 3-bits.
  Draw truth table
  Write logic equation
    P = S(1, 2, 4, 7)
x | y | z | P
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 26: Parity checking
If the given number contains an odd number of 1s the P is True. The given number is 3-bits.
  Draw truth table & write logic equation
  Simplify the equation with K-map
    P = x  y  z
1
1
1
1

## Slide 27: Digital Design Primer
FPGA/Verilog from Scratch
DAY 1 - LAB

## Slide 28: Outline
Hierarchical Design
Verilog Introduction
Structural Verilog
Lab exercises

## Slide 29: Hierarchical Design
Circuits are too complex for us to design all the detail at once.
Design subsystems for simple functions.
Compose subsystems to form the system
  Treating subcircuits as “black box” components
  Verify independently, then verify the composition
Topdown/bottomDigital Design Methodology — up design

## Slide 30: Summary
Digital systems use discrete (binary) representations of information.
Basic components: gates and flipflops
Combinational and sequential circuits
Real─ world constraints
  logic levels, loads, timing, area, etc
Verilog models: structural, behavioral
Design methodology
  Think
  Draw diagrams
  Write Verilog
  Test it

## Slide 31: verilog
Hardware Description Language (HDL)
  A computer language for modeling behavior and structure of digital systems
Verilog published in 1983, strong similarities to C.
Electronic Design Automation (EDA) using Verilog
  Design entry: alternative to schematics
  Verification: simulation, proof of properties
  Synthesis: automatic generation of circuits

## Slide 32: Module definition
A module is the main building block in Verilog
We first need to declare:
  Name of module
  Types of connections (inps , outps)
  Names of its connections
Verilog Module
A
B
C
Y

## Slide 33: Module definition
Verilog Module
A
B
C
Y

## Slide 34: Module definition
Positional association (implicit): parameters listed in the same order as the original module description
Explicit association: parameters explicitly listed in the arbitrary order.

## Slide 35: Verilog Syntax
Verilog is case sensitive: somename and SomeName are not the same!
Names can not start with numbers.
Whitespace is ignored.
Definition of multi-bits:

## Slide 36: Verilog Syntax
Use MSB to LSB ordering for busses (little-endian)
  A[31:0]
Define one module per file
  Makes managing your design hierarchy easier
Use a file name that equals module name
Develop/use a consistent naming style

## Slide 37: Number representation

## Slide 38: Number representation

## Slide 39: Data types
Nets connect components and are continuoly assigned values
  Wire is main net type
Variables store values between assignments
  Reg is main variable type
Scalar is a single value, usually one bit
Logic values: 0, 1, x (undefined state), z (tri-state/high impedance)

## Slide 40: Styles of verilog
Structural
  Describe how modules are interconnected
  Each module contains other modules (instances/submodules)
  Describes a hierarchy
Behavioral
  The module body contains functional description of the circuit
  Contains logical and mathematical operators
Practical circuits would use a combination of both!

## Slide 41: Structural verilog

## Slide 42: Structural verilog

## Slide 43: Structural verilog

## Slide 44: Structural verilog

## Slide 45: Structural verilog

## Slide 46: Structural verilog

## Slide 47: Structural verilog

## Slide 48: Testing on fpga board
Pay attention to the places marked with yellow.
Before we put it on the FPGA board, we need to specify which pins our inputs & outputs are connected to.
We have to perform the appropriate assignments from the pin planner using the user manual.
Main module (wants to run) select as a top module.

## Slide 49: Testing on fpga board
Led-switch example
One-two gates example