## Slide 1: Digital Design Primer
FPGA/Verilog from Scratch
DAY 2

## Slide 2: Outline
Combinational Circuits
Design Procedure
Adder , Subtractor , CRA
Comparator, Decoder , Encoder
FPGA

## Slide 3: COMBINATIONAL CIRCUITS
Consist of logic gates with outputs that are determined entirely by the present value of the inputs.
When input changes, output may change (after a delay).

## Slide 4: COMBINATIONAL CIRCUITS
Two important procedure
  Analysis: given circuit, find out its function
    Function may be expressed as:
      Boolean function
      Truth table
  Design : given the specifications, desired function, determine circuit.
    Function may be expressed as:
      Boolean function
      Truth table
?
?
?

## Slide 5: Desıgn procedure
Given a problem statement
  Determine the number of inputs and outputs.
  Derive truth table.
  Simplify the Boolean expression for each output.
  Produce the required circuit, draw the logic diagram.

## Slide 6: Binary adder
Half Adder
  Adds 1-bit plus 1-bit
  Produces Sum and Carry
x y | C S
0 0 | 0 0
0 1 | 0 1
1 0 | 0 1
1 1 | 1 0
x
y
S
C
HA
x
y
S
C
x
+ y
───
C S

## Slide 7: Binary adder
Full Adder
  Adds 1-bit plus 1-bit plus 1-bit
  Produces Sum and Carry
x
+ y
+ z
───
C S
FA
x
y
z
S
C
x y z | C S
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 0 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 1 0
1 1 0 | 1 0
1 1 1 | 1 1
 |  |  |  | y | 
 |  | 0 | 1 | 0 | 1
x |  | 1 | 0 | 1 | 0
 |  |  | z |  | 
 |  |  |  | y | 
 |  | 0 | 0 | 1 | 0
x |  | 0 | 1 | 1 | 1
 |  |  | z |  | 
S = xy'z'+x'yz'+x'y'z+xyz = x  y  z

## Slide 8: Binary adder
Full Adder
S
C
x
y
z
S
C
S = xy'z'+x'yz'+x'y'z+xyz = x  y  z
C = xy + xz + yz
x
y
z
c

## Slide 9: Binary adder
Full Adder
x
y
z
S
C
HA
x
y
z
HA
S
C

## Slide 10: Binary adder – 4bit
c3 c2 c1 .
+ x3 x2 x1 x0
+ y3 y2 y1 y0
────────
Cy S3 S2 S1 S0
FA
x3 x2 x1 x0
FA
FA
FA
y3 y2 y1 y0
S3 S2 S1 S0
C4 C3 C2 C1
0
Binary Adder
x3x2x1x0 y3y2y1y0
S3S2S1S0
C0
Cy
Carry Propagate Addition

## Slide 11: Binary subtractor
Use 2’s complement with binary adder
  x – y = x + (-y) = x + y’ + 1

## Slide 12: comparator
Compare 2-bit number to 2-bit number
  3 Outputs: < , = , >
  Expandable to more number of bits like 4-bit
Magnitude Comparator
A1A0 B1B0
A<B A=B A>B

## Slide 13: decoder
2-to-4 Line Decoder
I1 I0 | Y3 Y2 Y1 Y0
0 0 | 0 0 0 1
0 1 | 0 0 1 0
1 0 | 0 1 0 0
1 1 | 1 0 0 0
Binary Decoder
I1
I0
y3
y2
y1
y0

## Slide 14: multiplexers
MUX
Y
I0
I1
I2
I3
S1 S0
S1 S0 | Y
0 0 | I0
0 1 | I1
1 0 | I2
1 1 | I3

## Slide 15: multiplexers
2-to-1 MUX
4-to-1 MUX
MUX
Y
I0
I1
S
MUX
Y
I0
I1
I2
I3
S1 S0

## Slide 16: Implementation Using Multiplexers
Example F (x, y) = ∑(0, 1, 3)
MUX
Y
I0
I1
I2
I3
S1 S0
x y | F
0 0 | 1
0 1 | 1
1 0 | 0
1 1 | 1
x y
F
1
1
0
1

## Slide 17: FPGA
FPGA is a programmable logic device (PLD). PLD is a general purpose chip for implementing circuits and can be customized using programmable switches
Main types of PLDs
  PLA
  PAL
  ROM
  FPGA

## Slide 18: Programmable logic array (pla)
Use to implement circuits in SOP form
The connections in the AND & OR plane are programmable

## Slide 19: FPGA
Definition of field programmable gate array (FPGA): contains a matrix of reconfigurable gate array logic circuitry.
Why do we need FPGA?
  Alternative to custom IC
  Implemented in a short time
  using CAD tools

## Slide 20: FPGA
Programmable logic design process

## Slide 21: Digital Design Primer
FPGA/Verilog from Scratch
DAY 2 - lab

## Slide 22: Outline
Dataflow Verilog
Lab exercises
Modelsim Test

## Slide 23: Full Adder

## Slide 24: Full Adder

## Slide 25: Full Adder

## Slide 26: Full Adder

## Slide 27: Full Adder

## Slide 28: Adder/subtractor
Add new module: subtractor 4-bit.
Add overflow bit.
Running the design on the FPGA board.

## Slide 29: Comparing two numbers
Compare 4-bit number to 4-bit number
1 output: =
Part1:
  Draw truth table & write logic equation
  Simplify the equation with K-map
Part2:
  Implement the design with structural Verilog
  Running the structural design on the simulator.
  Implement the design with data flow Verilog
  Running the data flow design on the FPGA board.

## Slide 30: Comparing two numbers
Magnitude Comparator
A3A2A1A0 B3B2B1B0
A<B A=B A>B
Compare 4-bit number to 4-bit number
1 ouput =

## Slide 31: Comparing two numbers

## Slide 32: Comparing two numbers

## Slide 33: Comparing two numbers

## Slide 34: Comparing two numbers

## Slide 35: Comparing two numbers

## Slide 36: Comparing two numbers

## Slide 37: Write testbench
fullAdder_testbench.v
fullAdder.v
Logic blocks (filename.v)
  Wil be synthesized
  no # delaysexcept for registers
Testing blocks (filename_testbench.v)
  Pretty much anything goes
  Need # delay statements
Instantiate logic blocks inside testing blocks and drive the inputs and check outputs there

## Slide 38: Write testbench
fullAdder_testbench.v
fullAdder.v
Basic flow example for testbench

## Slide 39: Write testbench
A number of ways to verify designs
  Eyeball text printouts
    Quick and easiest
  Eyeball waveforms
    Quick and easy
  Write reference code and some other code to see if the two are the same. Make sure you temporarily force an error to test your setup.
    This is the most robust and what ius required for non-trivial designs.

## Slide 40: Write testbench
for 4-bit Full Adder write testbench and run on modelsim.

## Slide 41: Combinational design
Implement the design with structural or dataflow Verilog
You have to write these modules:
  Your main module
  _4nnand
  _4or
  _2to1_mux
Running the design on the FPGA board.